CNN
Stands for
Convolutional Neural Network (ConvNN)

---
CNN
Convolutional neural network (CNN) is a regularized type of feed-forward neural network that learns feature engineering by itself via filters (or kernel) optimization.
[Speaker Notes: A feedforward neural network (FNN) is one of the two broad types of artificial neural network, characterized by direction of the flow of information between its layers. Its flow is uni-directional, meaning that the information in the model flows in only one direction—forward—from the input nodes, through the hidden nodes (if any) and to the output nodes, without any cycles or loops, in contrast to recurrent neural networks(RNN), which have a bi-directional flow. Modern feedforward networks are trained using the backpropagation method and are colloquially referred to as the "vanilla" neural networks.]

---
CNN applications examples:
- image and video recognition
- image classification,
- medical image analysis,
- natural language processing

---
Architecture
Image Source: Medium.com
[Speaker Notes: The architecture of ConvNet is designed to take advantage of the 2D structure of an input image Architecture: Convolutional layer rectified linear unit (ReLU) activation function Pooling Layer Flatten Layer Fully Connected Layer]

---
Convolutional Layer
Convoluted Feature Map Image
Input Image
[Speaker Notes: Convolution is the process of combining two functions to produce the output of the other function A convolution is a grouping function in mathematics. Convolution occurs in CNNs when two matrices (rectangular arrays of numbers arranged in columns and rows) are combined to generate a third matrix.]

---
Applying filters Convolutional layer cont..
Input Image Size = 5 X 5
Filter Size = 3 x 3
Stride = 1
Padding = 0
Feature map size(output) = 3 x 3

---
Applying filters Convolutional layer cont..
Image Source: vitalflux.com
Input Image Size = 5 X 5
Filter Size = 3 x 3
Stride = 1
Padding = 1
Feature map size(output) = 5 x 5

---
Feature map size Convolutional layer cont..
Depends on:
- Input Image Size DI
- Filter Size DF
- Stride S
- Padding P

---
Stride Convolutional layer cont..
Stride: It denotes how many steps we are moving the filter at each step. [default is 1]
Stride = 1
Stride = 2

---
Padding Convolutional layer cont..
Padding is a process of adding (row or column) to the input at each side
Padding = 0
Padding = 1
Padding = 2

---
Padding Types Convolutional layer cont..
Same Padding
Valid Padding
Padding = 0
Padding = 1

---
Calculate Padding Convolutional layer cont..
P= { D_{i}*S - D_{i} + D_{f} - S} over {2}
let S = 1, P= {D_{f} - 1} over {2}

---
Calculate the feature map size

---
ReLU layer
- Applying max(0, x) on the previous feature map layers
- This one does not change size unlike the previous one

---
Pooling layer
- Its purpose is to gradually shrink the representation’s spatial size to reduce the number of parameters and computations in the network.
- The pooling layer treats each feature map separately.

---
Pooling layer methods (types)
- Max pooling
- Average Pooling
Source: Springer.com
[Speaker Notes: The following are some methods for pooling: Max-pooling: It chooses the most significant element from the feature map. The feature map’s significant features are stored in the resulting max-pooled layer. It is the most popular method since it produces the best outcomes. Average pooling: It entails calculating the average for each region of the feature map.]

---
Flatten Layer
Flatten is used to flatten the input. For example, if flatten is applied to layer having input shape as (3,3), then the output shape of the layer will be (9)
image source: superdatascience.com

---
Fully Connected layer
Is a fully connected neural networks – the classic neural network architecture, in which all neurons connect to all neurons in the next layer.

---
Resources
- Convolutional neural network [wikipedia]
- Feed-forward neural network [wikipedia]
- Basics of CNN in Deep Learning
- Intuitively Understanding Convolutions for Deep Learning
- Convolutional Neural Network CNN- الشبكات العصبية الملتفة by dr. Ahmed Yousry [youtube]
- What is ReLU and Sigmoid activation function?
- Convolutional Neural Networks (CNN): Step 3 - Flattening
- Feature map size calculate in CNN | Stride, Padding | Deep Learning Animation [youtube]
- Fully Connected Layers in Convolutional Neural Networks